Bluetooth Low Energy API
Open Vario

# History

Version	Date	Comments
1.0	01 nov. 2018	Open Vario GATT profile v1.0

# Glossary

BLE	Bluetooth Low Energy
API	Application programming Interface
GUID	Globally Unique Identifier
OS	Operating System
HW	Hardware
SW	Software
NA	Not Applicable
GAP	Generic Access Profile
GATT	Generic Attribute Profile

# Contents

# Overview

Open Vario is an open source variometer for paragliding and hang-gliding.
It can be remotely controlled using a Bluetooth Low Energy wireless link where it behaves as a GAP peripheral / GATT server device.
This document describes the GATT services and characteristics to access to Open Vario’s parameters and outputs.

# Data types

All the values described in this document have a fixed data type.
The following table describes all the data types used in the Open Vario BLE API:
Data type	Description	Size in bytes
int8	Signed 8 bits integer	1
uint8	Unsigned 8 bits integer	1
int16	Signed 16 bits integer	2
uin16	Unsigned 16 bits integer	2
int32	Signed 32 bits integer	4
uint32	Unsigned 32 bits integer	4
int64	Signed 64 bits integer	8
uint64	Unsigned 64 bits integer	8
float32	Single precision floating point value	4
float64	Double precision floating point value	8
bool	Boolean value with only 2 possible values: 0 = false, 1 = true	1
string	UTF-8 encoded string	-

The floating points data types are encoded according the IEEE 754 standard.
All the multi-bytes data types are encoded in little endian (i.e. less significant byte first).
All the strings have a maximum memory size and thus can be shorter than this maximum size. The trailing unused characters in the strings are filled with zeros.
Warning: a string which size is equals to its maximum size will have no trailing zero.
Any data type name followed by [] corresponds to an array of the data type.
The “Min” and “Max” columns in the following tables correspond to the minimum and maximum array size. This also applies to the string data type.
# Open Vario GATT profile

A Profile doesn't actually exist on the BLE peripheral itself, it’s only a predestined collection of services that are meant to be used together.
The Open Vario GATT profile compiles all the services needed to remotely control an Open Vario device.
The following illustration present the Open Vario GATT profile architecture:

Identification service
Feature service
Barometer service
Altimeter service
Variometer service
Navigation service
Flight data service
Flight storage service
Configuration service

Open Vario GATT profile
## Identification service
### GUID
{38df4da7-94f3-44dc-83ad-4e10864fbd44}
### Summary
The identification service exposes all the information needed to fully identify an Open Vario device.
### Characteristics
GUID	Name	Properties	Type	Min	Max	Unit
{520b42a8-ee29-46ec-9eff-24e732ca0cb5}	Software version	R	string	3	5	N/A
{dea233cc-dabb-4b00-9046-f70a44c1ceda}	Software manufacturer name	R	string	0	64	N/A
{26acdd71-ab60-4a9c-bb5b-101eecc43c00}	Open Vario GATT profile version	R	string	3	5	N/A
{77373005-83c6-4117-b8a9-04cc2be08224}	Hardware version	R	string	3	5	N/A
{82d07d5a-161a-40a8-b36f-9f816ec5d34f}	Hardware manufacturer name	R	string	0	64	N/A
{cbb12193-2b57-423e-8381-cc6996aee533}	Hardware serial number	R	string	0	64	N/A

### Functional description
This service is the only one which will be always available and which will always keep the same structure across the future versions of the Open Vario software.
The “Open Vario GATT profile version” characteristic purpose is to indicate the Open Vario GATT profile architecture in use on the Open Vario device and thus will permit to third party applications to use the corresponding API.
The version strings format is “AA.BB” where AA and BB are in the [0;99] interval.
The name and serial number strings have no pre-defined format.

## Feature service
### GUID
{4935b064-4e64-4385-8f2c-c2016b1c2e3d}
### Summary
The feature service exposes all the features provided by an Open Vario device.
### Characteristics
GUID	Name	Properties	Type	Min	Max	Unit
{8b7a91cd-90bd-4a53-97a0-6fcb4f845fbb}	Barometer service	R	bool	0	1	N/A
{62cff324-143b-4a25-afa8-34b4d6477e39}	Navigation service	R	bool	0	1	N/A
{43087328-8dcd-46bb-b80f-1af8cf2f3cdb}	Flight data service	R	bool	0	1	N/A
{20ff7952-b60a-49ce-8997-e4d4f36ac536}	Configuration service	R	bool	0	1	N/A

### Functional description
Each characteristic in this service indicates if the corresponding feature is available on the Open Vario device.

## Flight data service
### GUID
{7bb055f2-ab96-43ab-9ed4-f8dbaec1af10}
### Summary
The flight data service aggregates all the services which are exposing real time flight data information computed by the Open Vario device:
- Barometer service
- Altimeter service
- Variometer service
- Navigation service

### Barometer service
#### GUID
{d29a5ba1-e46c-4e2c-a1b7-05f21091a216}
#### Summary
The barometer service exposes all the barometric information computed by the Open Vario device.
#### Characteristics
GUID	Name	Properties	Type	Min	Max	Unit
{a59b4f7f-47ec-4515-b561-497209d3e8f2}	Pressure	R - N	uint32	0	200000	0.01 mbar
{88db8fd5-8362-429b-bfc8-c74aa6c2de44}	Temperature	R - N	int16	-400	1000	0.1 °C
{881a6d3a-83ac-47c6-87da-3d56470ffcd4}	Min temperature	R - N - W	int16	-400	1000	0.1 °C
{7248a65c-d483-425f-ab8b-917d010e90c5}	Max temperature	R - N - W	int16	-400	1000	0.1 °C

#### Functional description
The “Pressure” and “Temperature” characteristics’ values will be automatically updated by the Open Vario device.
The “Min temperature” and “Max temperature” characteristic’s values are computed by the Open Vario device. Any write (the written value is ignored) to one of these values will reset both values to the current value of the “Temperature” characteristic.

### Altimeter service
#### GUID
{516c5737-8250-493b-bb95-b2a16f65110e}
#### Summary
The altimeter service exposes the altitude information computed by the Open Vario device.
#### Characteristics
GUID	Name	Properties	Type	Min	Max	Unit
{f033de08-eda3-46a2-9918-19e123297152}	Main altitude	R - N – W	int16	-10000	10000	1 m
{8765ec19-d2ed-4c9e-8ac7-1f0c516a2d6b}	Min altitude	R - N – W	int16	-10000	10000	1 m
{067163e5-b097-4bd5-81a6-3fbf4dbfb6af}	Max altitude	R - N – W	int16	-10000	10000	1 m
{b176dd1b-d98e-4707-b51d-d0e31223f776}	Altitude 1	R - N – W	int16	-10000	10000	1 m
{e4c54ec3-e4b3-43a3-9eb0-9790615f68c3}	Altitude 2	R - N – W	int16	-10000	10000	1 m
{2a0934e3-7127-46c0-90a9-d6a5cbb51fa6}	Altitude 3	R - N – W	int16	-10000	10000	1 m
{80b81b29-791a-4b98-bc76-c6a85539b844}	Altitude 4	R - N – W	int16	-10000	10000	1 m

#### Functional description
The “Main altitude” characteristics’ value contains the primary altitude used for the computation of the “Altitude 1”, “Altitude 2”, “Altitude 3” and “Altitude 4” characteristic’s values and will be automatically updated by the Open Vario device.
A write operation can be made on this characteristic to calibrate the Open Vario device’s altitude computation.
The “Min altitude” and “Max altitude” characteristic’s values are computed by the Open Vario device. Any write (the written value is ignored) to one of these values will reset both values to the current value of the “Main altitude” characteristic.
The “Altitude 1”, “Altitude 2”, “Altitude 3” and “Altitude 4” characteristic’s values are secondary altitudes values which are relative to the primary altitude: any update of the primary altitude (either by the Open Vario device itself or by the BLE API) will trigger an update of the secondary altitudes. At contrary, any change made to the secondary altitude won’t have any impact to the main altitude. It will only update the secondary altitude value.

### Variometer service
#### GUID
{ae283ac8-786f-42ef-b694-b7faf492cae9}
#### Summary
The variometer service exposes the variometer information computed by the Open Vario device.
#### Characteristics
GUID	Name	Properties	Type	Min	Max	Unit
{7708157c-132f-4d21-a1d9-c9768732b4e9}	Vario	R - N	int16	-1000	1000	0.1 m/s
{4e149274-22f9-4185-b793-59a7b9e82db8}	Min vario	R - N - W	int16	-1000	1000	0.1 m/s
{bd98cd90-4d67-4b55-900a-204a75326b01}	Max vario	R - N - W	int16	-1000	1000	0.1 m/s
{9e13b15f-3582-433b-9034-55ac8881ee4f}	Acceleration	R - N	uint8	0	100	0.1 g
{12038fb7-12f6-49c5-8931-cae4af25019c}	Max acceleration	R - N - W	uint8	0	100	0.1 g

#### Functional description
The “Vario” and “Acceleration” characteristics’ values will be automatically updated by the Open Vario device.
The “Min vario” and “Max vario” characteristic’s values are computed by the Open Vario device. Any write (the written value is ignored) to one of these values will reset both values to the 0.
The “Max acceleration” characteristic’s value is computed by the Open Vario device. Any write (the written value is ignored) to one of this value will reset the value to 0.

### Navigation service
#### GUID
{530b9c7a-3185-49f0-9bb5-8e7b88a9df09}
#### Summary
The navigation service exposes the navigation information computed by the Open Vario device.
#### Characteristics
GUID	Name	Properties	Type	Min	Max	Unit
{609a0afe-59a2-4837-b4fe-46d2ddfec0dd}	Speed	R - N	uint16	0	600	0.1 m/s
{78b98321-3891-430b-a55d-3684f2cccdf8}	Min speed	R - N	uint16	0	600	0.1 m/s
{76f1298b-2ed1-44bf-b4b0-8281a18de6c4}	Max speed	R - N	uint16	0	600	0.1 m/s
{c75a49f0-cfe0-4d93-8109-3dbc588c2243}	Latitude (N)	R - N	float64	0	360	1 °
{3692fbda-6a27-4422-a307-5f852658cae0}	Longitude (E)	R - N	float64	0	360	1 °
{c6502b8c-5aae-489f-bb23-04eabc389f58}	Track angle	R - N	uint16	0	3600	0.1 °

#### Functional description
All the navigation information characteristics’ values will be automatically updated by the Open Vario device and cannot be modified.

## Flight storage service
### GUID
{34c03a57-1db2-4c2b-9eb5-a6ef8123b90d}
### Summary
The flight storage service exposes the flight data stored by the Open Vario device.
### Characteristics
GUID	Name	Properties	Type	Min	Max	Unit
{6e03badc-bce9-49cf-9cf1-2553249faf20}	Total number of flights	R – W	uint16	0	65535	N/A
{87163505-f11c-4621-973a-aa1e7e8e0a6d}	Current flight	R – W	uint16	0	65535	N/A
{f849a2e4-4c65-4df4-9b07-0c9c13aafbc0}	Take off time	R	datetime	N/A	N/A	N/A
{0eab8e50-c0d7-4672-a89a-ca310f85bf2e}	Landing time	R	datetime	N/A	N/A	N/A
{4da4039a-9069-491d-807f-bfb86399ebf0}	Min temperature	R	int16	-400	1000	0.1 °C
{14ba1834-7ded-493e-927f-54a0d69175ac}	Max temperature	R	int16	-400	1000	0.1 °C
{d45039f9-8c5b-4326-97f2-a33aa42483f8}	Min altitude	R	int16	-10000	10000	1 m
{af6408f1-1a8e-4cad-ab98-1775fd84a60e}	Max altitude	R	int16	-10000	10000	1 m
{e10adefb-3a62-4d4c-95c1-a00568eaee2e}	Min vario	R	int16	-1000	1000	0.1 m/s
{42f73fdb-1488-4bd7-9b3d-fc08011a7111}	Max vario	R	int16	-1000	1000	0.1 m/s
{25fd91b3-174c-4bb0-b7db-e6439283e54e}	Max acceleration	R	uint8	0	100	0.1 g
{7f717d6b-4a86-4d90-8b62-20cc55538234}	Flight data period	R	uint16	100	60000	ms
{507a9371-aa06-4cc7-93c5-33a189843619}	Total number of flight data	R	uint32	0	1000000	N/A
{299a5380-b4fe-4c09-a883-cecca2a8242f}	Current flight data	R – W	uint32	0	1000000	N/A
{14fd6e1d-45eb-4557-80d5-201ca8dc31ba}	Temperature	R	int16	-400	1000	0.1 °C
{2244b71c-27a1-42e9-a42c-2b81bc553507}	Altitude	R	int16	-10000	10000	1 m
{d1ea9e26-5207-4ba3-901d-58e1293c3913}	Vario	R	int16	-1000	1000	0.1 m/s
{9e42f3d7-a9ff-47ff-b458-8f4e0f7e7fac}	Acceleration	R	uint8	0	100	0.1 g
{ec86994e-2fd7-4757-8b71-579ed4c919d1}	Speed	R	uint16	0	600	0.1 m/s
{2717ddb8-ffa5-400c-8ff5-a7359abe98f9}	Latitude (N)	R	float32	0	360	1 °
{c12d6069-c308-4af2-b5c9-a80989074c29}	Longitude (E)	R	float32	0	360	1 °
{67ae725d-baf9-44cc-bdb9-406d2c743580}	Track angle	R	uint16_t	0	3600	0.1 °

### Functional description
The “Total number of flights” characteristics’ value correspond to the number of flights stored on the Open Vario device. A write to this characteristic with the value 0 will erase all the flights stored on the Open Vario device. Any other value will be ignored.
The “Current flight” characteristics’ value correspond to the current selected flight number in flights stored on the Open Vario device. A write to this characteristic with a value in the range [1; Total number of flights] selects the flight data to access. If “Total number of flights” is 0 or if the written value is outside the permitted range, the new value will be ignored.
Once a flight has been selected with the “Current flight” characteristic, the following characteristics will be updated by the Open Vario device with data of the selected flight:
- Take off time
- Landing time
- Min temperature
- Max temperature
- Min altitude
- Max altitude
- Min vario
- Max vario
- Max acceleration
- Flight data period
- Total number of flight data
- Current flight data
The “Current flight data” characteristics’ value correspond to the current selected flight data number in the current selected flights. A write to this characteristic with a value in the range [1; Total number of flight data] selects the flight data to access. If “Total number of flight data” is 0 or if the written value is outside the permitted range, the new value will be ignored.
Once a flight data has been selected with the “Current flight data” characteristic, the following characteristics will be updated by the Open Vario device with data of the selected flight data:
- Temperature
- Altitude
- Vario
- Acceleration
- Speed
- Latitude
- Longitude
- Track angle

## Configuration service
### GUID
{547d8117-3697-40ad-bf47-a8d6b6d3ae18}
### Summary
The configuration service exposes the configuration parameters of the Open Vario device and allows to modify them.
Warning: Some parameters are taken into account instantaneously, some are not and will need a power off or a reset to take effect. Please refer to the Open Vario parameters’ documentation for more information.
### Characteristics
GUID	Name	Properties	Type	Min	Max	Unit
{614ab7ea-1659-4ae6-8db8-cf1e628c04ed}	Reset to default values	W	uint32	0x52535456	0x52535456	N/A
{6dc4db82-17ba-45ae-90af-13c428fff96f}	Save values to non-volatile memory	W	uint32	0x53415645	0x53415645	N/A
{4985f149-be37-4515-a582-4566eca2d1e7}	Total number of parameter groups	R	uint8	1	255	N/A
{7751b07a-3c63-4767-89d9-ae730bb467d4}	Current parameter group	R – W	uint8	1	255	N/A
{60850c47-43b5-4995-9d75-471f2b8a0af8}	Parameter group’s name	R	string	1	32	N/A
{299e2bb6-92b9-48bb-97b3-dd40d5d2981f}	Total number of parameters	R	uint8	1	255	N/A
{d4c38506-9509-452a-97a3-4ba1455ca0ea}	Current parameter	R – W	uint8	1	255	N/A
{1791d595-b8a1-480c-88de-a833301f8e29}	Parameter’s name	R	string	1	32	N/A
{7d2587a1-f9c4-4b54-96a6-71384f53a161}	Parameter’s size	R	uint8	1	128	N/A
{4d8d332a-c7ed-462a-9633-5a28090960c3}	Parameter’s value	R – W	uint8[]	1	128	N/A

### Functional description
The “Reset to default values” characteristics’ value permits to reset all the parameters of the Open Vario device to their default values. Only the following value which corresponds to the ASCII string ‘RSTV’ will trigger the reset : 0x52535456. Any other value will be ignored.
The “Save values to non-volatile memory” characteristics’ value permits to save all the current parameters’ value of the Open Vario device into the non-volatile memory of the device so that they are preserved after a power-off or a reset. Only the following value which corresponds to the ASCII string ‘SAVE’ will trigger the reset : 0x53415645. Any other value will be ignored.
The “Total number of parameter groups” characteristics’ value correspond to the number of parameter groups stored on the Open Vario device.
The “Current parameter group” characteristics’ value correspond to the current selected parameter group in parameter groups stored on the Open Vario device. A write to this characteristic with a value in the range [1; Total number of parameter groups] selects the parameter group’s data to access. If the written value is outside the permitted range, the new value will be ignored.
Once a parameter group has been selected with the “Current parameter group” characteristic, the following characteristics will be updated by the Open Vario device with data of the selected parameter group:
- Parameter’s group name
- Total number of parameters
- Current parameter
The “Total number of parameters” characteristics’ value correspond to the number of parameters in the selected parameter group of the Open Vario device.
The “Current parameter” characteristics’ value correspond to the current selected parameter in the selected parameter group. A write to this characteristic with a value in the range [1; Total number of parameters] selects the parameter’s data to access. If the written value is outside the permitted range, the new value will be ignored.
Once a parameter has been selected with the “Current parameter” characteristic, the following characteristics will be updated by the Open Vario device with data of the selected parameter:
- Parameter’s name
- Parameter’s size
- Parameter’s value